## Slide 1: CND212: Digital Testing and Verification

## Slide 2: Digital IC Verification

## Slide 3: Introduction
Normal VLSI/Chip design flow

## Slide 4: The Verification Process
The process of checking that a given design correctly implements the specification and the required functionality.
A verification engineer accomplishes this by:
  Reading the hardware specification
  Creating a verification plan
  Building tests that show the RTL code correctly implements the features
Verification also includes error injection and handling.
  How does the design handle errors?
  How should it recover from them?
Verification consumes around 80% of the total product development time.

## Slide 5: What is Verified?

## Slide 6: Verification Levels
Basic verification: (at Unit/Sub-unit level)
Functional verification (at IP blocks level)
System level verification: (at the Systems level)
Connectivity: (at Board level)

## Slide 7: Verification Methods

## Slide 8: Verification Methods
Simulation Based Verification
Vivolo, L.. Transaction-based Verification And Emulation Combine For Multi-megahertz Verification Performance. [online] Electronicdesign.com. Available at: <https://www.electronicdesign.com/technologies/eda/article/21796417/transactionbased-verification-and-emulation-combine-for-multimegahertz-verification-performance>.

## Slide 9: Verification Methods
Formal Verification
It is a method by which we prove or disprove a design implementation against a formal specification or property by using a mathematical model.
An algorithm is used to explore all possible input values over time and to exercise all possible states in a design.
It works well for small designs where the number of inputs, outputs, and states is small.

## Slide 10: Verification Methods
Assertion-based Verification
An assertion is a statement about a design’s intended behavior, which must be verified.
It is a way of capturing a design’s intention or part of the design’s specification in the form of a property; this property can be used along with dynamic simulation and with formal verification to ensure whether this specification is met.
Assertions Benefits:
  Improves observability and debugging ability.
  Improves integration through correct usage checking.
  Improves verification efficiency.

## Slide 11: Verification Methods
Emulation Based Verification
Vivolo, L., 2021. Transaction-based Verification And Emulation Combine For Multi-megahertz Verification Performance. [online] Electronicdesign.com. Available at: https://www.electronicdesign.com/technologies/eda/article/21796417/transactionbased-verification-and-emulation-combine-for-multimegahertz-verification-performance.

## Slide 12: Verification Testbench
A Testbench is implemented to check the functional correctness of the DUT. This is achieved by doing the following:
  Generate stimulus
  Apply stimulus to the DUT
  Capture the response
  Check for correctness
  Measure progress against the overall verification goals
There are different approaches for testing:
  Directed Testing
  Pure Random Testing
  Constrained random stimulus
constrained

## Slide 13: Well Designed Verification Environment
Test Environment must:
  Be structured for debug
  Avoid false positives
Tests must:
  Achieve Functional Coverage
    Prevent untested regions
  Reach Corner Cases
    Anticipated Cases
    Error Injection
      Environment Error
      DUT Error
    Unanticipated Cases
      Random tests
    Be Robust, Reusable, Scalable
Testbench

## Slide 14: Verification Testbench
Transaction
  Class that holds a structure used to communicate with DUT.
  Then converted to pin-level data to be driven to the DUT or monitored.
Generator
  Creates or generates randomized transactions or stimuli and passes them to the driver.
Driver
  Interacts with DUT directly.
  Receives randomized transactions from the generator and drives them to the DUT as a pin-level activity.
Monitor
  Observe pin-level activity on the connected interface at the input and output of the design.
  Then, convert the pin-level activity into a transaction packet and send it to the scoreboard for checking purposes.
Top

## Slide 15: Verification Testbench
Test
  The test is at the top of the hierarchy, initiating the construction of the environment components and the connection between them.
  Responsible for the testbench configuration and stimulus generation process.
Testbench top
  The top-level component that includes interface and DUT instances.
  The design is connected to the testbench in the Top model.
Efficient Verification Testbench
  Layered.
  Reusable.
  Scalable.
  Easier to maintain.
Top

## Slide 16: SystemVerilog Basics

## Slide 17: SV Lexical Conventions
Same as Verilog
Case sensitive identifiers (names)
  Any sequence of letters, digits, $, and _
    First character cannot be a digit or $
  White spaces are ignored except within strings
Comments:
  Single line // ….
  Multiple lines /* …. */

## Slide 18: SV Number Format
Number format now supports sign/unsigned declaration
  <size>’[s|S]b (binary)
  <size>’[s|S]d (decimal)
  <size>’[s|S]h (hexadecimal)
  <size>’[s|S]o (octal)
  Can be padded with ‘_’ for readability
Sign Conversion
  signed’(myvar);
  unsigned’(myvar);
logic [7:0] my value; //defaults to unsigned
my_value = 8’b1; // 8’b0000_0001 (unsigned)
my_value = 8’sb1; // 8’b0000_0001 (signed)
//unsized padding of bits
my_value = ‘1; //8’b1111_1111
Notes: Without the [s|S] -> unsigned
With the [s|S] -> signed

## Slide 19: SV Data Types
SystemVerilog introduces new data types with the following benefits.
  Two-state: better performance, reduced memory usage
  Queues, dynamic and associative arrays and automatic storage: reduced memory usage, built-in support for searching and sorting
  Unions and packed structures: allows multiple views of the same data
  Classes and structures: support for abstract data structures
  Strings: built-in string support
  Enumerated types: code is easier to write and understand

## Slide 20: SV Data Types
Data type is a storage format having a specific range or type.
  Two states data type, each bit is
    Logic 0
    Logic 1
  Four states data type, each bit is
    Logic 0
    Logic 1
    Logic X; unknown (either 0/1)
    Logic Z; high impedance (floating)
Notes: Example when to use 2-state and 4-state

## Slide 21: SV Data Types: Four State (0|1|X|Z)
reg | logic [msb:lsb] variable_name [=initial_value];
4-state data type: logic | reg
  reg and logic are synonyms
  SystemVerilog improves the classic reg to have the following features:
    It can be driven by continuous assignments, gates, and modules, in addition to being a variable.
    It is given the new name logic so that it does not look like a register declaration.
Initialized to ‘x if initial value is not specified
Defaults to unsigned

## Slide 22: SV Data Types: Four State (0|1|X|Z)
Sized 4-state variable: integer, time
integer variable_name [=initial_value];
  32-bit signed
time variable_name [=initial_value];
  64-bit signed
integer a = - b;
time current_time;
b = -a;
current_time = $time;
If (current_time >= 100ms) ….. ;

## Slide 23: SV Data Types: Two State (0|1)
bit [msb:lsb] variable_name [=initial_value];
Better compiler optimizations for better performance
Variable initialized to ‘0 if initial_value is not specified
Assigned 0 for x or z value assignments
  Sized as specified
  Defaults to unsigned

## Slide 24: SV Data Types: Two State (0|1)
2-state-type variable_name [=initial_value];
Type | Description | Example
bit | user-determined range | bit [3:0] a_var;
byte | 8 bits, signed | byte a, b;
shortint | 16 bits, signed | shortint c, d;
int | 32 bits, signed | int i,j;
longint | 64 bits, signed | longint lword;

## Slide 25: SV Data Types: Two State (0|1)
2-state-type variable_name [=initial_value];
Type | Description | Example
shortreal | like float in C | shortreal f;
real | like double in C | real g;
realtime | identical to real | realtime now;

## Slide 26: SV Data Types: String Data Type
string variable_name [=initial_value];
Defaults to empty String “”
Can be created with $sformatf() system function
Built-in operators and methods:
  ==, !=, compare () and icompare()
  Itoa (), atoi, atohex () , toupper (), tolower (), etc.
  len (), getc (), putc (), substr ()

## Slide 27: SV Data Types: String Data Type
string variable_name [=initial_value];

## Slide 28: SV Data Types: String Data Type
string variable_name [=initial_value];

## Slide 29: SV Data Types: String Data Type

## Slide 30: SV Data Types: Enumerated Data Type
Define enum variables
enumtype variable_name [=initial_value];
  Date type defaults to int
  Variable initialized to ‘0 if initial_value is not
  specified (x for a 4-state data-type)
  enum can be displayed as ASCII or value
Define enumerated type
typedef enum [data_type] {named constants} enumtype;

## Slide 31: SV Data Types: Enumerated Data Type

## Slide 32: struct – Data Structure
Contains elements of different data types.
Struct is unpacked by default.
The new data type can be used throughout the code, avoiding editing in multiple places if required.
We can create a user-defined data type of a struct using typedef for multiple struct variables with the same contents

## Slide 33: struct – Data Structure

## Slide 34: struct – Data Structure
Packed structs
  struct defined with Packed keyword.
  Contains only packed data types.
  Variables are packed together in memory without gabs.

## Slide 35: union – Data Union
Like struct, contain different data types members,
But they share the same memory location.
Therefore,
  Memory efficient data structure.
  Restricts using one member at a time.

## Slide 36: union – Data Union

## Slide 37: Lab 1: ( ~ 60 min)

## Slide 38: Lab 1: design specs
In this lab, a model of communication protocol packet construction can be designed using the SystemVerilog data types. The model constructs and displays from 10 to 20 packets of random data.
Each packet contains the following:
  Packet ID: 0,1,2…
  Packet sent time.
  Packet data that is 32-bit width.
  Packet Type: Data, Command, Control.
The packets are constructed and displayed such that:
  The First packet type is Control.
  The second packet type is Command.
  The rest of the packets type is data