## Slide 1: CND212: Digital Testing and Verification

## Slide 2: SystemVerilog Routines

## Slide 3: Subroutines (task & function)
Tasks and functions provide the ability to execute common procedures from several different places in a code.
They also provide a means of breaking up large procedures into smaller ones to make them easier to read and debug.
Tasks and functions are collectively referred to as subroutines

## Slide 4: Subroutines (task & function)
Functions
  Cannot block
    Can’t have time-controlling statements such as @(posedge clk)
    The statements in the body of a function execute in one simulation time unit
  A non-void function must return a single value
    SystemVerilog improves this by adding (void function) which does not return a value
  Cannot enable a task
Tasks
  Can block
    May contain time-controlling statements
  Does not return a value
  Can enable other tasks and/or functions

## Slide 5: Subroutines (task & function) - example

## Slide 6: Subroutines (task & function) - example

## Slide 7: Task/function Memory Usage
Static
  Tasks/functions are static by default except if they are declared inside a class scope
  All variables of a static task/function are static by default
  Static variables retain their value between invocations
  There is a single static variable corresponding to each declared local variable in a module instance, regardless of the number of concurrent activations of the task/function.
  Static tasks/functions in different instances of a module have separate storage from each other
Automatic
  Allocate unique, separate storage for each task/function call
  All variables of an automatic task/function are automatic by default
  Automatic variables do not retain their values between invocations
  Automatic variables are replicated on each concurrent task/function invocation

## Slide 8: Task/function Memory Usage - example

## Slide 9: Functions vs Tasks - Summary
Function | Task
It cannot contain simulation delay, so it executes in the same time unit. | Can contain a simulation time delay and include time-controlling statements
Can return a single value unless it is a void function | Does not return a value but can achieve the same effect using output arguments
Cannot call another task | Can call another function or task

## Slide 10: SystemVerilog Threading

## Slide 11: fork – join (Parallel blocks)
There are two types of blocks in SystemVerilog
  Sequential blocks
    begin – end block
  Parallel blocks
    fork – join block
The parallel block is delimited by the keywords fork and join, join_any, or join_none.
The procedural statements in a parallel block is executed concurrently (in parallel)

## Slide 12: fork – join (Parallel blocks)
SystemVerilog provides three choices for specifying when the parent (forking) process resumes execution

## Slide 13: fork – join (Parallel blocks)

## Slide 14: fork – join (example1)
Example1: fork - join
fork block will be blocked until the completion of process-1 and Process-2.
Both process-1 and Process-2 will start at the same simulation time
  Process-1 will finish at 5ns
  Process-2 will finish at 20ns.
fork-join will be unblocked at 20ns.
Sequential blocks
Notes: When defining a fork-join block, encapsulating the entire fork within a begin-end block causes the entire
block to execute as a single process, with each statement executing sequentially

## Slide 15: fork – join_any (example2)
Example2: fork – join_any
The fork block will be blocked until the completion of any of the processes, Process-1 or Process-2.
Both Process-1 and Process-2 will start at the same simulation time,
  Process-1 will finish at 5ns
  Process-2 will finish at 20ns
fork-join_any will be unblocked at 5ns.

## Slide 16: fork – join_none (example3)
Example3: fork – join_none
The fork will start Process-1 and Process-2 at the same time, and it will come out of the block.
Process-1 and Process-2 will be executed until they are completed.

## Slide 17: fork – join (Parallel blocks)
Summary
For sequential blocks, the start time is when the first statement is executed, and the finish time is when the last statement has been executed.
For parallel blocks, the start time is the same for all the statements, and the finish time is controlled by the join construct used
Sequential and parallel blocks can be embedded within each other, allowing complex control structures to be expressed easily and with a high degree of structure.

## Slide 18: SystemVerilog Interprocess Synchronization & Communication

## Slide 19: Overview
Verilog provides basic synchronization mechanisms that are adequate at the hardware level (i.e. @)
This type of control is adequate for static objects but falls short in a dynamic and highly reactive testbench.
Hence, SystemVerilog adds the following communication mechanisms:
  Semaphores
    built-in class, which can be used for synchronization and mutual exclusion to shared resources
  Mailboxes
    built-in class, which can be used as a communication channel between processes

## Slide 20: Semaphore
semaphore identifier_name;
Conceptually, a semaphore is a bucket.
When a semaphore is allocated, a bucket containing a fixed number of keys is created
Processes using semaphores must first get a key from the bucket before executing.
All other processes must wait until a sufficient number of keys is returned to the bucket.

## Slide 21: Semaphore Methods
Method name | Description
new() | To create a semaphore with a specified number of keys
get() | To obtain or get a specified number of keys
put() | To put or return the number of keys
try_get() | Try to obtain or get a specified number of keys without blocking the execution

## Slide 22: Semaphore – Example 1

## Slide 23: Semaphore – Example 2
Get single key per process

## Slide 24: Semaphore – Example 3
Get multiple keys per process

## Slide 25: Mailbox
mailbox #(type) identifier_name;
A mailbox is a communication mechanism that allows messages to be exchanged between processes.
Data can be sent to a mailbox by one process and retrieved by another.
Mailbox behaves as first-in-first-out (FIFO), with a source and sink

## Slide 26: Mailbox Methods
Method name | Description
function new(int bound = 0) | Returns mailbox handle. An argument represents bounded mailbox size otherwise, it is an unbounded mailbox
task put(<data>) | Blocking method that stores data in the mailbox.
function int try_put(<data>) | The non-blocking method that stores data in the mailbox if it is not full and returns 1 else 0.
task get(ref <data>) | Blocking method to retrieve data from the mailbox
function int try_get(ref <data>) | The non-blocking method which returns data if a mailbox is non-empty else returns 0.
task peek(ref <data>) | Copies data from the mailbox without removing it from a mailbox
function int try_peek(ref <data>) | Tries to copy data from the mailbox without removing it from a mailbox
function int num() | Returns number of entries in the mailbox

## Slide 27: Mailbox – bounded/unbounded
Mailbox is unbounded by default.
It can be bounded by passing the required size to its new function.
A bounded mailbox becomes full when it contains the bounded number of messages.
  When the source thread tries to put a value into a sized mailbox that is full, that thread blocks until the value is removed.
  Likewise, if a sink threads tries to remove a value from an empty mailbox, that thread blocks until a value is put into the mailbox
Unbounded mailboxes never suspend a thread in a send operation.

## Slide 28: Mailbox – example

## Slide 29: Lab 3: (~ 60 min)

## Slide 30: Lab Task: Producer-Consumer Model
In this lab, a producer and consumer model can be designed using the pre-defined packet data type, SystemVerilog mailbox, and tasks as follows:
  Create a packet that has:
    ID
    Sent_time
    packet_type
    data
  Types of packets are:
    Message
    Command
    Control
  Create a task for a producer that writes in the mailbox every 10ns.
  Create a task for a consumer that reads from the mailbox every 5ns.
  Use fork-join to synchronize between them.
  Randomize multiple packets and send them from the producer in a fixed time interval.

## Slide 31: Assignment: (~ 60 min)

## Slide 32: Assignment: Producer-Consumer Model with priorities
For the lab assignment, a producer and consumer model can be designed using the pre-defined packet data type, SystemVerilog mailbox, and tasks as follows:
  Create a packet that has: ID, Sent_time, packet_type, priority and data.
  Types of packets are Message, Command, and Control.
  There are three levels of priority:
    High
    Medium
    Low
  Create a task for a producer that writes in the mailbox every 5ns
  Create a task for a consumer that reads from the mailbox every 20ns but reads the packets with higher priority first.
  Use fork-join to synchronize between them.
  Randomize multiple packets and send them from the producer in a fixed time interval.