## Slide 1: CND212: Digital Testing and Verification

## Slide 2: Coverage Driven Verification (CDV)
CDV is one of the main critical criteria for Judging the effectiveness of applied verification methodology and helps us identify what “Hasn’t been tested.”
Classified into two main types:
1. Code coverage
2. Functional coverage.
Both types of coverage metrics are essential for assessing the completeness and quality of the verification.

## Slide 3: Code Coverage
Code coverage is a completion metric that indicates how much of the code of the Design Under Test (DUT) has been executed.
It does not indicate that the code is correct.
Types of RTL code coverage:
    Statement coverage
    Conditional coverage
    Branch coverage
    Path coverage
    Toggle coverage
    FSM coverage

## Slide 4: Code Coverage: Statement coverage
Measures the percentage of code statements that have been executed during the simulation.
From N lines of code and according to the applied stimulus how many statements (lines) are covered in the simulation.
Line coverage includes only the executable statements.
Statements which are not executable like module, end module, comments, timescale etc are not covered.

## Slide 5: Code Coverage: Statement coverage
There are total 12 statements at lines
5, 7, 8, 11, 13, 14, 15, 17, 19, 20, 21, 22 Covered 9 statements: 5, 7, 8, 11, 13, 14, 17, 19, 21 Uncovered 3 statements: 15, 20, 22 Statement coverage percentage: 75.00 (9/12)

## Slide 6: Code Coverage: Conditional coverage
Conditional coverage is the ratio of no. of cases checked to the total no. of cases present.
Suppose one expression having Boolean expression like AND or OR, so entries which is given to that expression to the total possibilities is called expression coverage.

## Slide 7: Code Coverage: Conditional coverage
At LINE 13: Combinations of STATEMENT c = (b && a)
B = 0 and a = 0 is Covered
B = 0 and a = 1 is Covered
B = 1 and a = 0 is Not Covered
b = 1 and a = 1 is Not Covered
At LINE 14: combinations of STATEMENT if ((c && f))
C = 0 and f = 0 is Covered
C = 0 and f = 1 is Not Covered
C = 1 and f = 0 is Not Covered
C = 1 and f = 1 is Not Covered
Total possible combinations: 8
Total combinations executed: 3

## Slide 8: Code Coverage: Branch coverage
At line 15 branch b = e; not covered
At line 17 branch e = b; covered
At line 20 branch 1: f = 1; not covered
At line 21 branch 0: f = 0; covered
At line 22 branch default: f = 0; not covered
Coverage percentage: 40.00 (2/5)

## Slide 9: Code Coverage: Path coverage
Path 1 : Not Covered
Path 2 : Not Covered
Path 3: Not Covered
Path 4: Not Covered
Path 5 : Covered
Path 6 : Not Covered
Total possible paths : 6
Total covered path : 1
Path coverage Percentage : 16.67 (1/6)

## Slide 10: Code Coverage: Toggle coverage
Name Toggled 1->0 0->1
  a No Yes
  b No No
  c No No
  d No No
  e No No
  f No No

## Slide 11: Code Coverage: FSM coverage
In this coverage we look for how many times states are visited, transited and how many sequence are covered in a Finite state machine.
Two Types:
  1. State Coverage:
It gives the coverage of no. of states visited over the total no. of states.
  2. Transition Coverage:
It will count the no. of transition from one state to another and it will compare it with other total no. of transition.

## Slide 12: Code Coverage: FSM coverage

## Slide 13: Code Coverage: FSM coverage
FSM coverage report for the above example:
// state coverage
s1 | Covered
s2 | Not Covered
s3 | Covered
s4 | Covered
// state transition
s1->s2 | Not Covered s3->s1 | Not Covered
s1->s3 | Covered s3->s4 | Covered
s2->s1 | Not Covered s4->s1 | Covered
s2->s4 | Not Covered
@4 S1
@5 S1
@15 S1
@25 S3
@35 S4
@45 S1

## Slide 14: Code Coverage: Summary
Achieving high code coverage does not guarantee the correctness of the design or the absence of bugs.
It is possible to have high code coverage but still have functional bugs that were not exercised during testing.
In addition, code coverage does not take into account the design's corner cases and error handling.

## Slide 15: Functional Coverage
There are two types of functional coverage:
  1. Cover property
Checks whether sequences of behaviors have occurred.
Using SystemVerilog Assertions.
  2. Covergroup
Checks combinations of data values have occurred. We can get Data- oriented coverage by writing Coverage groups, coverage points and also by cross coverage

## Slide 16: Functional Coverage: Cover property

## Slide 17: Functional Coverage: Covergroup
The covergroup construct is a user-defined type. The type definition is written once, and multiple instances of that type can be created in different contexts.
A covergroup instance can be created via the new() method.
A covergroup can be defined in a module, program, interface, or class.
Each covergroup specification can include the following components:
    Clocking event
    Coverage points
    Cross coverage
    Arguments(optional)
    Coverage Options

## Slide 18: Covergroup: Clocking event
A clocking event that synchronizes the sampling of coverage points

## Slide 19: Covergroup: Clocking event
The expression within the iff construct specifies an optional condition that disables coverage for that cover point.
In the preceding example, cover point "cp_varib" is covered only if the value reset is low.

## Slide 20: Functional Coverage: Coverage Points
Each coverage point is associated with “bin”. On each sample clock simulator will increment the associated bin value.
Bins can be created implicitly or explicitly
Implicit Bins
- While define cover point, if you do not specify any bins, then Implicit bins are created.
- For an “n” bit integral coverpoint variable, a 2^n number of automatic bins will get created.
- The number of bins creating can be controlled by auto_bin_max parameter.

## Slide 21: Coverage Points: Implicit Bins

## Slide 22: Coverage Points: Implicit Bins
for addr: c1.auto[0] c1.auto[1] c1.auto[2] … c1.auto[255]
for wr_rd: c2.auto[0]

## Slide 23: Coverage Points: Explicit Bins
Explicit bin creation is recommended method.
Not all values are interesting or relevant in a cover point, so when the user knows the exact values he is going to cover, he can use explicit bins.
You can also name the bins.
“bins” keyword is used to declare the bins explicitly to a variable.
Two types:
1. Value Bins
2. Transition Bins

## Slide 24: Coverage Points: Explicit Bins

## Slide 25: Coverage Points: Explicit Bins
Array of Bins

## Slide 26: Coverage Points: Explicit Bins
Fixed number of bins

## Slide 27: Coverage Points: Explicit Bins
SystemVerilog allows specifying one or more sets of ordered value transitions of the coverage point.
Type of Transitions:
  Single Value Transition
  Sequence Of Transitions
  Set Of Transitions
  Consecutive Repetitions
  Range Of Repetition
  Goto Repetition
  Non Consecutive Repetition

## Slide 28: Coverage Points: Explicit Bins
Single Value Transition

## Slide 29: Coverage Points: Explicit Bins
Sequence Of Transitions

## Slide 30: Coverage Points: Explicit Bins
Set Of Transitions

## Slide 31: Coverage Points: Explicit Bins
Consecutive Repetitions

## Slide 32: Coverage Points: Explicit Bins
Range Of Repetition

## Slide 33: Coverage Points: Explicit Bins
Goto Repetition

## Slide 34: Coverage Points: Explicit Bins
Non Consecutive Repetition

## Slide 35: Coverage Points: Explicit Bins
Ignore Bins

## Slide 36: Coverage Points: Explicit Bins
Illegal Bins:

## Slide 37: Functional Coverage: Cross Coverage
Cross allows keeping track of information which is received simultaneous on more than one cover point.
Measures what values were seen for two or more cover points at the same time.
Note that when you measure cross coverage of a variable with N values, and of another with M values, SystemVerilog needs N*M cross bins to store all the combinations.

## Slide 38: Functional Coverage: Cross Coverage

## Slide 39: Functional Coverage: Arguments
Generic coverage groups can be written by passing their traits as arguments to the coverage constructor. This allows creating a reusable coverage group which can be used in multiple places.

## Slide 40: Functional Coverage: Options
Coverage Options |  |  | 
Option | Syntax | Description | Default
Weight | weight= number | If set at the covergroup syntactic level, it specifies the weight of this covergroup instance for computing the overall instance coverage of the simulation. If set at the coverpoint syntactic level, it specifies the weight of a coverpoint for computing the instance coverage of the enclosing covergroup | 1
Goal | goal=number | Specifies the target goal for a covergroup instance. | 100
Name | name=string | Specifies a name for the covergroup instance. | 

## Slide 41: Functional Coverage: Options
Coverage Options |  |  | 
Option | Syntax | Description | Default
Comment | comment=string | A comment that appears with a covergroup instance. | 
At_least | at_least=number | Minimum number of hits for each bin. | 1
Auto_bin_max | auto_bin_max=number | Maximum number of automatically created bins. | 64
Per_instance | per_instance=Boolean | Each instance contributes to the overall coverage information for the covergroup type. If true, coverage information considered per each instance. | 0

## Slide 42: Functional Coverage: Methods
Coverage Methods | 
Method | Description
void sample() | Triggers sampling of the covergroup
real get_coverage() | Method returns the cumulative (or type) coverage, which considers the contribution of all instances of a particular coverage item, and it is a static method.
real get_inst_coverage() | Method returns the coverage of the specific instance on which it is invoked, thus, it can only be invoked via the "." operator.
void start() | Starts collecting coverage information
void stop() | Stops collecting coverage information

## Slide 43: Coverage Reports on VCS
Home > Synopsys > Open in terminal > gedit filename.sv
Write your code and save.
In the terminal write the next commands:
Compilation command:
vcs -sverilog -cm line+cond+fsm+tgl filename.sv
Simulation Command:
./simv -cm line+cond+fsm+tgl
Command to generate Coverage report: Coverage report in html format will be in the ./urgReport directory
urg -dir simv.vdb
Open interactive Verdi to track coverage
Verdi –cov –covdir simv.vdb &

## Slide 44: Assignment
Your task is to design a testbench for a given RTL (Register Transfer Level) code of a finite state machine and create a set of cover groups. The goal is to cover the states, state transitions, and output signals of the finite state machine.